## Slide 1: HEP-Frame A Software Engineered Framework to Aid the Development & Efficient Multicore Execution of Scientific Code
André Pereira
António Onofre
Alberto Proença

## Slide 2: Presented in Las Vegas (Dec 9)

## Slide 3: Agenda
Motivation
Presenting HEP-Frame (Highly Efficient Pipeline Framework)
HEP-Frame with a Real World Case Study
Conclusions and Future Work

## Slide 4: Motivation (1)
The development of efficient scientific code requires techniques from
  High Performance Computing: to process data in the least time possible
  High Throughput Computing: to process more data per time unit
To achieve this goal we need
  Knowledge from the scientific/engineering domain
  Clear definition of the application requirements
  Efficiency-centered design of algorithms and data structures

## Slide 5: Motivation (2)
Structure of scientific applications (our view)
  Handle independent datasets
  Execute a chain of tasks (a pipeline)
  Each task execution may depend on other(s)
Real world examples
  Modeling/simulation
  Quantitative data analysis

## Slide 6: Motivation (3)
Computational Scientist
  Expert in the requirements of a scientific field
  Limited knowledge on sustainable parallel code
Software Engineer
  Expert on code design and development
  Limited knowledge on the end user domain and requirements
Notes: orientador de cada extremo, eu no meio

## Slide 7: HEP-Frame
A move from a resource-centered to a user-centered framework
Aiming to aid the development of sustainable parallel pipelined code
Key goals:
  To provide an user-friendly interface, hiding from the end user hardware details
  To bet on performance with an hybrid HPC/HTC approach, addressing issues of compute, memory and I/O bound applications
  To dynamically address efficiency issues across different computing platforms, adapting features from the best resource-centered frameworks (undergoing...)

## Slide 8: HEP-Frame Design (1)
To aid code development (compile time)
  Providing an user-friendly interface
  Implementing app specific features
  Coding abstractions
To aid efficient code execution (runtime)
  Single core automatic optimizations
  Shared memory automatic parallelization (current prototype)

## Slide 9: HEP-Frame Design (2)
To aid code development (compile time)
  Providing an user friendly interface
  Implementing app specific features
  Coding abstractions
To aid efficient code execution (runtime)
  Single core automatic optimizations
  Shared memory automatic parallelization (current prototype)

## Slide 10: HEP-Frame Efficiency Features (1)
Inter-dataset optimizations (aiming HTC)
  Replicate pipeline to process independent dataset elements
  Use OpenMP with dynamic scheduler (suited for irregular workloads)
  Balance/mix processes with threads (research undergoing)

## Slide 11: HEP-Frame Efficiency Features (2)
Intra-dataset optimizations (aiming HPC)
  Removal of algorithmic and data structures inefficiencies
  Exploring the parallel hardware at each core (ILP, SIMD, ...)
  Adequate ordering of the pipeline tasks
Pipeline can be described with Linear Temporal Logic
  FGP1 ∧ FGP2 ∧ ... ∧ FGPn
  If proposition P2 depends on P1
  F GPn ∧...∧F G(P1 ∧F GP2 )

## Slide 12: HEP-Frame Efficiency Features (3)
Pipeline reorganization mechanism
  Propositions execution time
  Propositions filtering ratio
Graph of propositions
  Dependencies represented as “infinite” weight
  Best order is a path through all propositions that minimizes the overall weight
  Hamiltonian Path (NP-Complete) with simplifications
proposition weight

## Slide 13: Real World Case Study (1)
A particle physics data analysis
  Developed by CERN physicists of the ATLAS Experiment
  Studies the couplings of top quarks to the Higgs boson (ttHdilep)
Computational characteristics
  17 simple propositions to filter non complying data
  1 heavy proposition that reconstructs the collision

## Slide 14: Real World Case Study (2)
Report on porting (by a physicist)
  15-minute crash course
  4 hours to port an implementation
  Changes to the framework did not require updating the physicist code
  Final framework learning curve no longer than 30 minutes

## Slide 15: Execution Times with HEP-Frame
Intel Xeon | E5520 | X5650 | E5-2650v2 | E5-2670v2 | E5-2695v2
Key data | 2x4 cores @2.27GHz | 2x6 cores @2.67GHz | 2x8 cores @2.6GHz | 2x10 cores @2.5GHz | 2x12 cores @2.4GHz
Sequential Exec. Time (s) | 215 | 196 | 175 | 180 | 183
Parallel Exec. Time (s) | 45 | 30 | 23 | 22 | 23
Execution of the ttHdilep code
Distinct compute nodes in a cluster, all with dual Xeons
Parallel version: one single process using all available cores, no SMT
Computing accelerators (GPU, Intel MIC): under development

## Slide 16: HEP-Frame Efficiency
Comments on this plot
  “Number of Cores”: max available cores at the compute node
  1-core: reference sequential throughput
  Previous code improvements (without HEP-Frame) achieved speedup <8 for 20 cores
  Low performance due to thread synchronization and I/O inefficiencies
Notes: general rules

## Slide 17: HEP-Frame Pipeline Reorganization
Reordering at runtime
  70% performance improvement
  Reduces the amount of variables recorded per proposition
  The algorithm requires some time to converge
Initial Order | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | Total Time
Exec. Time (ms) | 37113 | 1,03 | 0,70 | 1,53 | 0,97 | 8,04 | 0,48 | 5,13 | 0,43 | 5,60 | 0,44 | 1,35 | 0,40 | 0,53 | 0,28 | 0,38 | 0,56 | 91055 | 175 s
Element Pass % | 100 | 100 | 100 | 100 | 50,4 | 99,9 | 100 | 100 | 100 | 100 | 99,7 | 94,9 | 99,5 | 99,9 | 99,2 | 100 | 63,4 | 100 | 
Reorder Result | 5 | 17 | 12 | 15 | 13 | 11 | 14 | 6 | 16 | 1 | 2 | 3 | 4 | 7 | 8 | 9 | 10 | 18 | 
Exec. Time (ms) | 0,97 | 0,60 | 0,86 | 0,18 | 0,25 | 0,26 | 0,33 | 4,76 | 0,24 | 2111,9 | 0,31 | 0,21 | 0,45 | 0,28 | 3,03 | 0,26 | 3,31 | 91033 | 101 s

## Slide 18: Conclusions
HEP-Frame eases the development of sustainable parallel code
  Provides a user-friendly interface
  Addresses execution efficiency issues transparently from the user
Small learning curve for Computational Scientists
ttHdilep port to HEP-Frame achieved a speedup of 8x for a 20-core system
  Using a general heuristic for pipeline applications, rather than tailored optimizations
  Efficiency still limited by synchronization and I/O
Pipeline reorganization improved the execution time of ttHdilep by 70%

## Slide 19: Key Topics for Future Work
Improve the reorder mechanism
  To make it converge faster
  To reduce its overhead
Improve efficiency with hybrid HTC/HPC
  Hybrid multiprocess/multithread parallelization (first prototype recently completed)
  Automatic offload of compute intensive propositions to computing accelerators

## Slide 20: HEP-Frame ?
ampereira@di.uminho.pt